## Slide 1: SMART INVENTORY LEVEL SYSTEM
MIGUEL LOPEZ

## Slide 2: PROBLEM?
Retail Store environment
  Stockroom inventory levels fluctuate daily
  Inbound shipment units must be monitored manually
  Help coordinate stockroom management efforts

## Slide 3: SYSTEM DESIGN
Track each shelf with weight sensors
Report to main system at beginning of day
Visualize and log data

## Slide 4: SYSTEM DIAGRAM

## Slide 5: LOAD CELLS
3 Wire load cells
50kg each
200kg = about 440 lbs.

## Slide 6: MODULE - MCU - MICROCOMPUTER
HX711
  Amplify the analog signals
  Connected through data pin and clock
ESP8266
  Wifi microcontroller
Raspberry Pi
  Mosquitto -> Node-Red -> InfluxDB -> Grafana

## Slide 7: FLOW CHART OF DATA
All software running on the Raspberry Pi

## Slide 8: TROUBLES
HX711 system was not reliable
  Tried multiple example codes, became confusing fast
  Fault in module? Fault in 1 sensor? 2 sensors?
    # of sensors used determine wiring layout

## Slide 9: COMPROMISES
Simulated results of HX711/weight sensors
No touchscreen display for manual control
No automatic visualization

## Slide 10: FUTURE TINKERING
Get HX711 working, apply to different projects?
MQTT dashboard/control from android?
Some functional level of the touchscreen display
Alternative MQTT broker?
  Hosted on android or traditional x86/x64 Linux | Windows

## Slide 11: Mosquitto
MQTT subscription messages being stored by NodeRed and stored into an InfluxDB database

## Slide 12: Node-RED
Converting string to num in NodeRed, to then store into InfluxDB, and read as nums and not string by Grafana

## Slide 13: Grafana
Short Live Demo